## Slide 1
Smart CAPEX OMA
Densification
Functional documentation
20/12/2023

## Slide 2
Technical Module
1
Technical to Economical Module
2
Economical Module
3
Summary
Smart CAPEX OMA

## Slide 3
1
Smart CAPEX OMA
Technical Module

## Slide 4
This document integrates the methodology conceptualization of modules 0, 1-9 and the implementation approach of remaining items
End-to-end workflow
Application interface
Technical to economical conversion modules
Economic modules
Technical modules
Value driver impact quantification
ARPU: Quantification of ARPU uplift, for neighbor sites next to created site. ARPU uplift is calculated according to neighbor sites clients ARPU
Gross margin quantification
Quantification of economic value at site based on value driver improvement and site margin
A. ARPU
Site NPV quantification
Quantification of Site NPV considering cell gross margins, costs and financial factors
8
7
9
Data Quality
Data collection quality check
Collect data
check the consistency of the data in terms of nomenclature
check network data repository
check the distribution of traffic data (missing, extreme or outlier values)
0
Preprocessing
Preprocessing of hourly OSS data and Weekly OSS data (FDD/4G or TDD)
1
Densification - Network status:
Once RANDim has given us the predicted network state and the achievable upgrades (capacity and densification), we reuse this file to find the ideal location for these new densification sites.
Traffic improvement
Deployment effect on traffic at site and cluster level based on Capacity KPIs
Traffic forecasting
Network load and quality forecast by technology and service
2
5
4
Modeling
Training the impact model of a densification site and applying the model to the neighbors of each new site
6
Congestion Analysis
Use the RANDim tool to calculate the congestion of each cell
3
Smart capex workflow diagram
**However, we are aware that coverage can be implemented to calculate the effects on the site itself, and that these steps may take some development time. (between step 8 and 9)

## Slide 5: Technical functionalities
Conceptualization considering OMA specificities
Estimation of net traffic evolution by use case (TDD / FDD) on neighbor sites (2 nearest sites) analyzing different site attributes
  Traffic forecasting
1
Forecast of traffic and capacity KPIs by cell on a weekly basis for the coming two years using Prophet algorithm per use case (FDD/TDD)
  Traffic improvement
Outputs
  Traffic evolution for data at neighbor site level after the densification action
  Data traffic
  Congestion detection and Selection of upgrade action
Detect congestion based on RANDim tool. Then the RANDim tool provide us the suggestion of site creation, with location, to answer the congestion on site that capacity upgrades can’t resolve (Densification)
  New site location, with congested cells affected by this site creation
  Oss preprocessing
Process historical data with two granularity (Weekly and Hourly). Moreover, we need to consider FDD(4G) and TDD use case We managed in this phase to have a unique and stable identifier for each cell.
  Preprocessed OSS counters:
    Unique cell identifiers
    One file per use case (FDD/TDD)
    One file per granularity (Weekly/Hourly)
2
3
4

## Slide 6
Smart CAPEX OMA
OSS Preprocessing

## Slide 7: OSS counters are processed per granularity and use case (FDD/TDD)
This step includes the processing of various raw data files with different granularity (weekly/hourly) and different use case(TDD/FDD)
For weekly granularity we necessitate at least two years of historical data for integration into the forecasting model.
For Hourly granularity we necessitate at least 1 week of historical data for integration into the RANDim tool
Historical OSS at Weekly granularity
Filter on cell_name
to catch TDD cells
Filter on cell_band
to catch 4G cells
Processed OSS weekly TDD
Processed OSS weekly FDD
OSS Hourly TDD
OSS Hourly FDD
Processed OSS hourly TDD at busy hour
Processed OSS hourly FDD at busy hour

## Slide 8
Smart CAPEX OMA
Traffic forecasting

## Slide 9: Traffic and capacity KPI are forecasted for each cell on weekly basis for the coming two years
data traffic
Data traffic download at each cell aggregated on weekly basis
Forecasted traffic will be used to calculate a ratio of evolution per cells
This ratio will help us to have a projection of hourly data to a precise future period
  ML model: Prophet Model
Inputs
Forecast based on historical data at weekly granularity for both use case (FDD / TDD)

## Slide 10
Données Manquantes
Données Aberrantes / Atypiques
Données Eligibles
Distribution study and search for missing observations
Identifying and Handling Outliers
Representativeness test
Training Data
Start date– End date
Test data
Start date– End date
Validation criteria of a successful model
Estimation Additive Model Yt=Tt+St+εt
the trend Tt corresponding to a long-term evolution of the series (Linear, Quadratic, Logarithmic)
the seasonality St to be estimated
the error εt which is the random part of the series
Traffic forecasting using the model chosen in the previous step
Cell_2
Cell_1
Cell_3
OSS COUNTER
Data Audit & Reliability
Modeling
Forecasting
1
1
TRAFFIC FORECASTING – METHODOLOGY

## Slide 11
Densification – Traffic forecasting: Résultats (Similaire à Capacity)
Objectifs
  Prédire les KPIs de traffic et de congestion :
    A la résolution hebdomadaire
    Pour chaque cellule issue de OSS Preprocessing
    Pour les deux prochaines années
Critères d’acceptance
  Erreur de prédiction < 15 % sur la plage Mars à Novembre 2023
Résultats
  Le résultats du traffic forecasting ont été validé sur une base tech/mensuel sur l’ensemble de 67204 cellules de Mars 2023 à Novembre 2023.
  Les erreurs moyennes :4% pour la voix, 8% sur la data dl 5% sur la data ul
Revue des critères d’acceptance
  Erreur de prédiction moyenne de 5.6%
  sur la plage Mars à Novembre 2023 : OK
Equation du modèle prophet
représentes la tendance de la série, la saisonnalité annuelle, la saisonnalité hebdomadaire, la saisonnalité quotidienne, l’effet vacances, jour fériers et l’erreur
Métrique de validation
La métrique de validation est l’AEP: Absolute Error Percentage (AEP) qui est adaptée à notre tâche prédictive.
est la valeur réelle, est la valeur prédite.

## Slide 12
Smart CAPEX OMA
Congestion detection and site densification

## Slide 13
Titre
Lorem ipsum dolor sit amet, consectetur adipiscing sed.
Sed rhoncus, nisi eu facilisis condimentum.
Titre
Lorem ipsum dolor sit amet, consectetur adipiscing elit.
Sed rhoncus, nisi eu facilisis condimentum, ligula augue porttitor lacusamet, ligula consectetur porttitor.
Filtre des sites congestionnés à la date
future d’ajout capacitaire (M+6)
02
Preparation of data for the new site proposition
Predicted traffic KPIs (2 years)
Compute_rate
Enable us to project our hourly data to a period by calculating a ratio from weekly data between historical data and the forecasted data at this period
Congestion detection
RANdim
Use RANDim tool on our projected hourly data to find out the congested sites
Densification proposition
RANDim
Use RANDim output to another RANDim request to get the densification proposition
01
03

## Slide 14: Compute rate – Projection of hourly data
Data preparation for RANDim
The calculation of congestion and new site propositions are done with RANDim tool.
RANDim tool use as input hourly data preprocessed to get busy hour.
However, we cannot forecast our hourly data on 2 years horizon, so we :
Forecast weekly data on two years horizon
Select a period we want look at
Calculate an evolution ratio between forecasted weekly data and historical data per cells
Apply this ratio to our hourly data at busy hour formatted by RANDim
Historical data end : 202305
Period we look at : 202350
Ratio = 894 / 725 = 1,23
Chart: Week period

## Slide 15: Get congestion and densification suggestion
Data usage by RANDim
We use RANDim tool for the congestion detection and then densification suggestion.
Initialisation of RANDim tool
We have a first interaction with RANDim tool where we give the hourly data at busy hour and RANDim result is a configuration file and our hourly data file rearange under RANDim format.
Congestion Detection
This file outputed by the first RANDim call is then project to a futur period with the ratio calculated from the weekly historical and forecasted data.
This projected hourly file is then give to RANDim to obtain the congestion of the network.
Densification proposition
This congestion file is given to a new RANDim request and give us as result the densification suggestions where we find the new site location and the nearly congested cells that need a new sites to decongest themself.

## Slide 16
Densification Randim Results
Sample of Result
Résultats proposés par Randim
Nombre de nouveaux site proposés: 38
Nombre de site décongestionnées: 37
Nombre de cellules de décongestionnées: 46
Pour information, on ne travaille qu’avec la 4G

## Slide 17
Smart CAPEX OMA
Traffic improvement

## Slide 18: Traffic improvement estimation
Chart: 
 | 2 | 4 | 6 | 8 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
 | 14 | 16 | 18 | 20 | 22 | 22 | 22 | 22 | 22
Traffic
Traffic improvement
Action
Impact duration
Investment recovery time
Y2
Y4
Stabilization period (e.g. 4 weeks)
Y1
Y3
Y5
Traffic improvement
Data traffic improvement
e.g. Traffic increment for year 4
Once impact duration has ended, the increment of traffic will be constant for the remaining years
Year 1
Year 2
Year 3
Year 4
Year 5
∆ Data
traffic (GB)
100
110
120
130
130

## Slide 19: Traffic improvement estimation
The first approach is to look at the evolution of the traffic on the 2 neighours sites after the creation of a new site. The approach is called the « capacity » approach. In a second time the « coverage » approach should be developed to evaluate the trafic generated by the new site created.
Site created
2 nearest sites
Capacity approach
Coverage approach
Furthest site

## Slide 20: Evolution of neighbor data traffic is forecasted based on the technical site archetype, traffic status before the action and the upgrade action
Site archetype
Technical attributes: e.g., configuration before the action, existing bands and existing techs, etc.
Pre-action status
Traffic: e.g., Average traffic, traffic standard deviation, etc.
Upgrade action
Traffic: Traffic volume on both neighbor sites after the new site creation

## Slide 21
CAPACITY – Gain de traffic grâçe à l'ajout capacitaire (upgrade)
Objectifs
  Estimation du gain du trafic suite aux nouveaux site densifiés
  1 Modèle pour la data downlink
  Intégration de l’effet tendance régionale dans l’estimation de ce gain
Scope du protocole de validation :
Données de 01/2021 à 07/2023
  639 sites utilisés pour la construction du modèle
  72 sites utilisés pour la validation (10 % du total)
Technologies : 4G
2 modèles de Machine Learning spécifiques testés (Random Forest et XGBoost)
Résultats :
Data : R² = 0,87 (Test validation)
Chart: Data Downlink

## Slide 22
2
Smart CAPEX OMA
Tehnical to Economical Module

## Slide 23: This document integrates the methodology conceptualization of module 7
End-to-end workflow
Application interface
Technical to economical conversion modules
Economic modules
Technical modules
Value driver impact quantification
ARPU: Quantification of ARPU uplift, for neighbor sites next to created site. ARPU uplift is calculated according to neighbor sites clients ARPU
Gross margin quantification
Quantification of economic value at site based on value driver improvement and site margin
A. ARPU
Site NPV quantification
Quantification of Site NPV considering cell gross margins, costs and financial factors
8
7
9
Data Quality
Data collection quality check
Collect data
check the consistency of the data in terms of nomenclature
check network data repository
check the distribution of traffic data (missing, extreme or outlier values)
0
Preprocessing
Preprocessing of hourly OSS data and Weekly OSS data (FDD/4G or TDD)
1
Densification - Network status:
Once RANDim has given us the predicted network state and the achievable upgrades (capacity and densification), we reuse this file to find the ideal location for these new densification sites.
Traffic improvement
Deployment effect on traffic at site and cluster level based on Capacity KPIs
Traffic forecasting
Network load and quality forecast by technology and service
2
5
4
Modeling
Training the impact model of a densification site and applying the model to the neighbors of each new site
6
Congestion Analysis
Use the RANDim tool to calculate the congestion of each cell
3
**However, we are aware that coverage can be implemented to calculate the effects on the site itself, and that these steps may take some development time. (between step 8 and 9)

## Slide 24: Technical to economical conversion functionalities varies by type of value driver
Quantification of ARPU uplift, at neighbor sites level, based on traffic impact (data) of each neighbor site and corresponding unitary revenue considering the neighbor site's clients ARPU and expected evolution in time
Conceptualization considering OMA specificities
Value drivers impact quantification
5
Outputs
ARPU increase for data, at year, neighbor site level
ARPU

## Slide 25: Contexte: Technical to Economical module
For a 5 years business plan [2024 --- 2028]
In the technical module:
– Additional traffic due to the upgrade
– Increase of additional traffic following the regional traffic increase rate
In the technical-to-economical module:
– We apply unit prices to obtain total revenue increase after upgrade per action
– We compute economical kpis (revenue, opex) for a reference year
Scope:
- 38 affected sites, xx actions
- 4G technology

## Slide 26: Revenue estimation approach based on traffic

## Slide 27: ARPU increase is quantified comparing the neighbor sites revenues resulting from traffic improvement and those before the action
Year 1
Year 2
Year 3
Year 4
Year 5
∆ Data
traffic (GB)
100
110
120
130
130
∆ Data
Revenue ($)
500
550
600
650
650
∆ Revenue/ ARPU Data (%)
Year 0 site revenue: 4500$
Data unitary revenue: 5 $/GB
Recap| Traffic improvement by service
Chart: 
 | 2 | 4 | 6 | 8 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
 | 14 | 16 | 18 | 20 | 22 | 22 | 22 | 22 | 22
Traffic
(action)
Impact duration
Investment recovery time
Y2
Y4
Stabilization period
(4 weeks)
Y1
Y3
Y5
∆ Y2
∆ Y1
Once impact duration has ended, the increment of traffic will be constant for the remaining years
∆ Y5=
∆ Y4
∆ Y3
∆ Y4
11.1%
12.2%
13.3%
14.4%
14.4%

## Slide 28
3
Smart CAPEX OMA
Economical Module

## Slide 29: This document integrates the methodology conceptualization of module 7
End-to-end workflow
Application interface
Technical to economical conversion modules
Economic modules
Technical modules
Data Quality
Congestion Analysis
Use the RANDim tool to calculate the congestion of each cell
Value driver impact quantification
ARPU: Quantification of ARPU uplift, for neighbor sites next to created site. ARPU uplift is calculated according to neighbor sites clients ARPU
Gross margin quantification
Quantification of economic value at site based on value driver improvement and site margin
A. ARPU
Site NPV quantification
Quantification of Site NPV considering cell gross margins, costs and financial factors
8
7
9
Data collection quality check
Collect data
check the consistency of the data in terms of nomenclature
check network data repository
check the distribution of traffic data (missing, extreme or outlier values)
0
Preprocessing
Preprocessing of hourly OSS data and Weekly OSS data (FDD/4G or TDD)
1
Densification - Network status:
Once RANDim has given us the predicted network state and the achievable upgrades (capacity and densification), we reuse this file to find the ideal location for these new densification sites.
Traffic improvement
Deployment effect on traffic at site and cluster level based on Capacity KPIs
Traffic forecasting
Network load and quality forecast by technology and service
2
5
4
Modeling
Training the impact model of a densification site and applying the model to the neighbors of each new site
6
Congestion Analysis
Use the RANDim tool to calculate the congestion of each cell
3
**However, we are aware that coverage can be implemented to calculate the effects on the site itself, and that these steps may take some development time. (between step 8 and 9)

## Slide 30: Complete conceptualization of all economic modules
Conceptualization
Outputs
  Site NPV quantification
9
  NPV calculation is performed for each upgrade action considering incremental effects:
    Incremental gross value generated by the action (module 6)
    Incremental OPEX for energy or space rent as well as CAPEX considering historical values
    Financial time factors (e.g, WACC, average lifetime, corresponding impact duration and investment recovery time etc.)
  Site NPV
  Annual cashflows
  Site allocated CAPEX
  Annual OPEX
  Gross margin quantification
8
  Increase in ARPU results in a proportional increase of the average margin per client calculated at neighbor site level
  Site/cell economic variables (e.g., revenue, margin) calculated adding the weighted values of the clients based on their consumption
    The client margin to be used in this context only includes marginal costs
    Sites' margins to be used on ARPU modeling are calculated in two steps
  Site margins Annual
  Gross values

## Slide 31: Increase in ARPU results in a proportional increase of the average margin per client
ARPU uplift
=
∆ ARPU year n considering site characteristics
Annual site margin for corresponding service
X
Site gross value add due to ∆ ARPU per year
Each year will have a different ∆ARPU driven by traffic improvement and change on unitary revenues
Weighted margin of clients by service based on traffic consumption
∑
Voice
Data
7
Economic modules
Gross margin quantification - ARPU
8
(∆ traffic year n * average price year n )
∆ ARPU year n =
Annual site revenue for corresponding service in year 0
See the next slide for more details (last two columns on the right)

## Slide 32: NPV calculation is performed for each upgrade action considering incremental effects
Site Upgrade action's NPV
Incremental annual OPEX linked to the action
Site gross annual margin generated by the action
  Annual cashflow affected by recovery time discount rate
Incremental CAPEX linked to the action
)
∑
ARPU
uplift
  Incremental CAPEX linked to each upgrade in terms of HW requirements
  Incremental OPEX linked to each upgrade in terms of:
  Energy
  Space rent
(
Computed at site level
  Discount rate: Parameter (e.g. 13%)
  Recovery time: Parameter defined based on most restrictive criteria (e.g. 5 years)
Economic modules
  Site NPV quantification
9

## Slide 33: NPV calculation is performed for each upgrade action considering incremental effects
Site Upgrade action's NPV
Incremental annual OPEX linked to the action
  Annual cashflow affected by recovery time discount rate
Incremental CAPEX linked to the action
)
∑
  Incremental CAPEX linked to each upgrade in terms of HW requirements
  Incremental OPEX linked to each upgrade in terms of:
  Energy
  Space rent
(
  Discount rate: Parameter (e.g. 13%)
  Recovery time: Parameter defined based on most restrictive criteria (e.g. 5 years)
Site gross annual margin generated by the action
ARPU
uplift
Computed at site level
Economic modules
  Site NPV quantification
9
ARPU uplift

## Slide 34: NPV calculation is performed for each upgrade action considering incremental effects
Site Upgrade action's NPV
Site gross annual margin generated by the action
  Annual cashflow affected by recovery time discount rate
Incremental CAPEX linked to the action
)
∑
ARPU
uplift
  Incremental CAPEX linked to each upgrade in terms of HW requirements
(
Computed at site level
  Discount rate: Parameter (e.g. 13%)
  Recovery time: Parameter defined based on most restrictive criteria (e.g. 5 years)
Economic modules
  Site NPV quantification
9
Incremental annual OPEX linked to the action
  Incremental OPEX linked to each upgrade in terms of:
  Energy
  Space rent

## Slide 35: Opex definition
7
Economic modules
Site NPV quantification
9
 | Band | Opex énergie
2G | G900 | 750
3G | U900 | 500
 | U2100 | 500
4G | L800 | 850
 | L1800 | 750
 | L2600 | 850
 | Total | 4200
Our energitical opex represent 4200 DH per month
We need to add to this value 3000 DH per month for maintenance and management fees.
Thus, our monthly Opex are 7200 DH per month

## Slide 36: NPV calculation is performed for each upgrade action considering incremental effects
Site Upgrade action's NPV
Incremental annual OPEX linked to the action
Site gross annual margin generated by the action
  Annual cashflow affected by recovery time discount rate
)
∑
ARPU
uplift
  Incremental OPEX linked to each upgrade in terms of:
  Energy
  Space rent
(
Computed at site level
  Discount rate: Parameter (e.g. 13%)
  Recovery time: Parameter defined based on most restrictive criteria (e.g. 5 years)
Economic modules
  Site NPV quantification
9
Incremental CAPEX linked to the action
  Incremental CAPEX linked to each upgrade in terms of HW requirements

## Slide 37: Capex definition
7
Economic modules
Site NPV quantification
9
The capex, defined with the stackholders, were define as in the table.
Thus, our capex is equal to 0,249 + 0,12 = 0,369 MMAD, so 369 000 DH
Band | Capex Radio MMAD
G900 + U900 + U2100 + L1800 + L800 | 0,249
L2600 | 0,12

## Slide 38: Thank you